## Slide 1: Multiprotocol Label Switching (MPLS) Fundamentals and Futures
Adrian Farrel
April 3, 2016

## Slide 2: AGENDA
A history lesson
Basic building blocks
  Data plane
  Control planes
Developments, changes, extensions
Current status
The future for MPLS

## Slide 3: Once upon a time in a land far, far away…
I like telling stories!
Routers were originally built to handle forwarding in software on a single CPU
  Bottleneck as port speeds increased
Ipsilon mapped IP traffic to ATM circuits to achieve a faster “IP switch” in 1996
Cisco’s “Tag Switching” is similar but not limited to ATM technology
  IP flows are associated with a “tag” using a control protocol
  Packets/cells have a tag attached to them and can be switched at L2 rather than routed at L3
    Faster fixed-length lookup vs. longest-prefix match
IETF worked to standardise the solutions and develops MPLS
  Curiously, IP switching speed is no longer a motivation
  We have since discovered new uses for “IP virtual circuits”
  First IETF RFC on MPLS published in March 1999
    RFC 2547 “BGP/MPLS VPNs”
    The application pre-dated the architecture!
      RFC 3031 “Multiprotocol Label Switching Architecture” April 2001

## Slide 4: The MPLS Data Plane
It’s a simple encapsulation at “layer 2.5”
Forwarding is based on a simple look-up
  {incoming interface, incoming label}  {outgoing interface, outgoing label}
IP Header
Shim Header
Data Link Header
Data
Label (20 bits)
Stack (1 bit)
TTL (8 bits)
TC (3 bits)
7
3
2
9

## Slide 5: The Magic of MPLS Labels
Label operations are simple but powerful
  Push (impose) a label at ingress
  Swap and forward at transit
  Pop (strip) at egress to reveal the payload
    Pop-and-go (penultimate-hop-popping)
The label imposed at the ingress defines the path through the network
  We say “Label Switched Path (LSP)”
Labels can be stacked
  Allows aggregation, tunnelling, fine-grain meaning
Labels can have magic meanings
  Special Purpose Labels
  “If you find this label do something special with the packet”

## Slide 6: The Job of the MPLS Control Plane
How does a router know what label to include in a packet?
Special purpose labels are well-known
Other labels must be “agreed” between routers
  “When I send label X, you must take the following action”
Labels are normally chosen by the receiver and advertised to the sender
  Downstream label allocation
Upstream label allocation also exists
  Useful on multi-access links
The control plane protocols advertise the labels and their usage
A management plane approach is also available
  Central control (also known as SDN)

## Slide 7: Label Distribution Protocol - Fundamentals
Installs an LSP to match each shortest forwarding path learned from the IGP
LSPs ‘merge’ towards the destination forming a destination-based tree
LDP uses managed sessions with neighbours running over TCP
  Neighbours may be remote using tunnels (hence label stacks)
LDP advertises a label and a Forwarding Equivalence Class (FEC)
  A FEC is a route
    An address
    A prefix
    A set of prefixes
  All packets matching a FEC are ‘classified’ and treated the same
  There is no demultiplexing feature

## Slide 8: Traffic Engineering with MPLS
TE is a well established practice in transport networks
Objectives are to improve network efficiency, increase traffic performance, avoid faults and maintenance, reduce costs, and increase profitability
Component elements
  Measurement and Characterization
  Modeling and Planning
  Control
Widely achieved through MPLS
  Connection-oriented Packet Switching (CO-PS)
RSVP-TE is the protocol of choice
  Originally a soft-state protocol which leads to scaling concerns (state and processing)
  Largely resolved through protocol improvements and better implementations
Introducing the Path Computation Element (PCE)
  Distributed and centralised path computation for request/response and control
PCE

## Slide 9: BGP/MPLS VPNs
Each PE advertises
  The VPN instances served
  The prefixes reachable per VPN
  A Route Reflector may be used
An MPLS label indicates for which VPN the traffic is intended
  Important at PE2
Traffic is directed across the core to the right PE for the {VPN, prefix}
  Can use LDP LSPs to reach the PE
  Can use traffic engineered LSPs (RSVP-TE)
    This leads towards a full-mesh of LSPs between all PEs
Each packet has a label stack
  Top label is the tunnel across the core
  Next label identifies the VPN (and hence the VRF)
  Further label may provide “pop-and-go” routing
Widely deployed (famously RFC 2547 the first MPLS RFC)
VPN A
VPN A
VPN A
VPN B
VPN B
PE 1
PE 4
PE 3
PE 2
VPN A

## Slide 10: Time Passes – MPLS Feature Creep
As with all successful technologies new uses emerge
Each new application demands new tweaks to control plane protocols
  Pseudowires
  Fast Reroute
  Entropy Label
  Basic OAM
  Point-to-multipoint LSPs
  MPLS Transport Profile (MPLS-TP)
  Advanced VPNs

## Slide 11: Pseudowires
A type of virtual private line
  Emulated service between CEs
    May carry and Ethernet or signal-based service over a packet-based network
Access connections are real wire connections or services
  CEs consider themselves directly attached
PEs exchange MPLS labels using LDP (remote adjacencies)
  Label identifies all packets for the emulated service
MPLS tunnel between PEs
  Could be LDP or RSVP-TE
The rest is just encapsulation
  Label stack
  Control word
  Data depending on type
MPLS Tunnel
Customer Network
Provider Network
CE
PE
Emulated Services
Access Connections
Pseudowire LSPs

## Slide 12: Fast Reroute
Use MPLS Tunnels to protect LSPs when resources fail
  Link and Node protection
  Typically need to use TE tunnels
Can protect multiple LSPs in one tunnel
Protection is “fast” because protection tunnel is already in place
  “Simply” switch packets from a physical interface to a logical interface
Published RFC is an amalgam of two solutions
  Facility backup protects a single resource with a tunnel
  LSP backup protects each LSP with a tunnel
It may be considered complex to manage and operate
  Lots of configuration, tricky protocol behaviour, complex OAM
  Typically only used to protect key or vulnerable spots
  May be assisted using PCE and central controller
Bypass tunnel
Merge point
Point of Local Repair
Bypass tunnel
Merge point
Point of Local Repair

## Slide 13: Entropy Label
Load balancing is an important feature in today’s networks
  Fat LSPs need to be spread across links to make space for other LSPs
  LSPs are often fatter than the links that carry them
But…
  Traffic flows demand in-order packet delivery
  Usual technique is to hash on the packet header
  But…
    Label stacks are sometimes too deep to reliably hash right down to the flow identifier
    Some flows need to be kept together
    Some devices can’t do enough hashing at line speed
The entropy label can be inserted into the label stack to enhance hashing
  Actually, it’s two labels
    A special purpose label to say don’t forward on this label
    The entropy label itself

## Slide 14: Basic OAM
LSP Ping
  Similar to IP ping
  Echo request is a packet sent on an LSP to the egress
    It is wrapped in UDP and IP and labelled exactly as a data packet
    Destination address of the IP packet is 127/8 to cause it to be handled locally
  Echo reply is send back by any route
    It is UDP in IP and can be forwarded as IP or sent down an LSP
    It is sent to the sender of the Echo Request
  Provides Connectivity Check (CC) and Connectivity Verification (CV)
  Can trace routes by using TTL expirey
BFD is a packet data plane OAM protocol
  Capable of much more rapid fault detection than LSP Ping
  Configured or bootstrapped by LSP Ping

## Slide 15: Point-to-Multipoint (P2MP)
LDP is essentially multipoint-to-point
  Flows converge onto labels towards the destination
RSVP-TE is essentially point-to-point
New extensions have been devised for P2MP
RSVP-TE P2MP
  Uses small protocol extensions
  Allows planned trees useful for content distribution
LDP P2MP
  Immediately becomes Multipoint-to-multipoint

## Slide 16: MPLS-TP
What is a “transport profile”?
  Switching not forwarding?
  Operational familiarity?
  Connection-oriented?
  High availability and protection switching?
  OAM?
  Central control and management?
  Static LSPs?
Who specifies requirements, solutions, deployments?
  What happens if there is a lack of coordination in specification?
IETF
ITU

## Slide 17: MPLS-TP Work
Operation without an IP control plane
  This largely means static provisioning
    Replace an IP-based control plane with an IP-based management plane?
    This is a TE (CO-PS) approach
    Compare with SDN
Development of additional OAM mechanisms
  An in-band OAM channel called the Generic Associated Channel (G-ACh)
    A special purpose label the Generic Associated Channel Label (GAL)
      Indicates this is not a packet to be forwarded
    Followed by the Associated Channel Header
      Contains a “channel type”
        MCC
        SCC
        BFD control
        MPLS loss measurement, delay measurement, CC, CV, etc.
  Specification of various OAM and protection switching message-based protocols

## Slide 18: Advanced VPNs
VPN features and functions have grown rapidly
  Results in a complex set of features and options
    Comparing services can be hard
    Achieving vendor interoperability needs care
Multi-AS support
Multicast support
Scaling mechanisms to avoid full-mesh concerns
  Hub-and-spoke
Layer 2 VPNs
  Pseudowire connectivity
  VLANs
  Ethernet VPNs (EVPNs) using BGP/MPLS

## Slide 19: MPLS Today
“Most packets on the Internet today traverse an MPLS network at some point in their journey”
“No router vendor can be taken seriously unless they have extensive MPLS offerings”
“MPLS VPN connectivity is a commercially significant service offering”
Scaling of the MPLS control and forwarding planes are as critical to product choice as other factors such as route table scaling
However, some operators (tier 1 and tier 2) remain resolutely IP only

## Slide 20: MPLS Futures
Support for IPv6
Network Security
SDN
Service Function Chaining
Segment Routing
Ring Protection Mechanisms

## Slide 21: MPLS and IPv6
MPLS is agnostic about what traffic it carries
  So IPv6 can be carried over an LSP with no additional work
MPLS control plane protocols were “designed with IPv6 in mind”
  They did need a little fixing in specifications and implementation
    Now good to go and widely tested
Not clear how many IPv6 control planes will be run in the immediate future
  But one day there will be plenty
  MPLS is ready

## Slide 22: MPLS Network Security
Strong dependency on ACLs and “known peers”
  Control plane address space
Control plane security
  LDP and BGP over TCP (TLS, TCP-AO, …)
  Some minor patches/clarifications to LDP
  RSVP-TE hop-by-hop security
Data plane security
  Largely ignored in favour of L2, L3, and application security
    MACsec under
    IPsec over
    End-to-end in the application layer
  Experimenting with MPLS Opportunistic Security

## Slide 23: MPLS in an SDN World
SDN at the network layer means central control
  Not necessarily Traffic engineering
There are two views
  Central control of LSPs provisioned through the control plane
  Central control of switching/forwarding in the NEs
Many tools exist that can be put to use
  IGPs report resource availability as usual
  BGP-LS can report the topology for planning and computational purposes
  PCE can compute resource uses, supply paths for LSPs, and command the control plane
  RSVP-TE to set up LSPs
  Multiple southbound possibilities
    Netconf/YANG
    PCEP
    I2RS
    BGP
    Even OpenFlow?
PCE Controller/Orchestrator
RSVP-TE
BGP-LS
PCEP

## Slide 24: Service Function Chaining
SFC is the process of steering traffic to off-path servers or devices
  This allows virtualisation of functions previously deployed in dedicated hardware as “bumps on the wire”
    Cost savings
    More agile to new functions, updates, bug-fixes
Principal requirement is to identify the traffic flows so that they can be directed to the servers or devices in the right order
  For packets on each flow, the server needs to know:
    Which functions to invoke and in which order
    Where to send the packets next and how to mark them
This can be simply achieved using MPLS
  It is very much like a BGP VPN function
  The ingress classifies the packets and imposes two labels
    For a tunnel to the next server
    For the Service Function Chain
  Each server is programmed with instructions for the SFC
    BGP (via a route reflector) can be used to program the servers

## Slide 25: Segment Routing
A new way to use the MPLS data plane unchanged
  Basic operation is “pop label, look-up next label, send packet”
Each router or link can be assigned a “label”
  Labels can be distributed with the IGP
Ingress can select a path by imposing a label stack
Central controller can instruct ingress about stack to impose
Label stack might become large
  Use “loose hops” to a remote node
  Use “virtual links” (multi-hop LSP tunnels) assigned a “label”
    Transit operation becomes “pop label, impose new label stack, send packet”
124
93
317
67
Payload
67
Payload
67
317
Payload
67
317
93
Payload
67
317
93
124
Payload
Payload

## Slide 26: Resilient MPLS Rings
Packet rings are increasingly used
Rings are special environments for protection
  When a link or node fails, traffic can be routed around the ring the other way
Current proposal suggests rings can self-discover
Bidirectional full circuit LSP tunnels are used
Traffic entering the ring at any point is placed on the LSP to its point of egress
In the event of a failure
  New traffic is sent the other way
  Traffic at the point of failure is looped back to go the other way around the ring
1
6
4
5
3
8
2
7

## Slide 27: The Long View
Technologies come and technologies go
  In the end we’ll all retire, anyway
Things we know
  IPv4 will yield to IPv6
  ATM died because it was too complex and the frames too small
Things that are happening may squeeze MPLS
  More and more features are being added to Ethernet
  There is a strong push to add quality and determinism to IP
  Continued growth in MPLS features risks complexity
There is plenty of life left in MPLS
  Continued growth in applicability and deployment

## Slide 28: Questions?
afarrel@juniper.net